## Slide 1: Android and Robotics
Make Stuff, Have Fun
Jay Dellinger
google.com/+JayDellinger
@DellingerTech
#AnDevCon

## Slide 2: A Bit About Me
Jay Dellinger
B.S. Aerospace Engineering
Lockheed Martin Aeronautical Systems (3 years)
Dellinger Technologies LLC (15 years)
Manheim (14 years)
Notes: Manheim is the world’s leading provider of vehicle remarketing services.
Over 110 locations worldwide in 16 countries, we handle nearly eight million vehicles annually.

## Slide 3: Agenda
General Robotics
Android as robotic component
Solving problems with robots
Development of a prototype
  Arduino
  Raspberry Pi
  Android
Wrap Up/Review

## Slide 4: General Robotics
Robot
“a machine that can do the work of a person and that works automatically or is controlled by a computer.”
-Merriam-Webster

## Slide 5: General Robotics
Android
“A mobile robot usually with a human form.”
-Merriam-Webster

## Slide 6: Robots Among Us
Toys
  Animatronics
  Lego Mindstorms
  Sphero
Home Automation
  Climate Control
  Roomba
Manufacturing
  Assembly
  Quality Control
Automotive
  Vehicles
  Traffic Signals
Military & Police
  Bomb disposal
  Drone aircraft
Others…
You will find plenty of robots around you every day

## Slide 7: Robots In the News
Space probes and Planetary Exploration
Amazon Drone Delivery
  FAA regulations ~2015
Google Driverless Vehicles
Google Robotics Acquisitions
  8 robotics companies

## Slide 8: Robots In Fiction
Star Wars
Transformers
Robocop
Wall-E
I, Robot
Terminator
Etc., Etc., Etc…
Ubiquitous in our entertainment which feeds general expectations…for better or worse.

## Slide 9: Three Laws of Robotics
A robot may not injure a human being or, through inaction, allow a human being come to harm.
A robot must obey the orders given to it by human beings, except where such orders would conflict with the first law.
A robot must protect its own existence as long as such protection does not conflict with the first or second law.
- Isaac Asimov

## Slide 10: Android as Robotics Platform
Embedded Android on custom boards
Standard Android device as an onboard controller
Standard Android device as a remote controller

## Slide 11: Robotics vs Software Concepts
Integration of multiple systems
Specialization of components
Inputs/outputs
Model-View-Controller

## Slide 12: Innovation Day
Problem: Large vehicle lots filled with cars
Goal: Timely information on vehicle location
Considerations
  Hard wired sensor tracking (RFID)
  Mobile scanning of RFID
  Robotic approaches
  Visual vs non-visual scanning
  Autonomous vs manual control
Application of external interests as potential solution

## Slide 13: Prototype Development
Problem: small vehicle controlled from my device with live video feed
Solution: Impossible! (let’s break this down a bit)
Components
  Chassis with wheels and motors
  Some way to control motors
  Video stream
  Android app as controller
This is a contrived example but serves to illustrate the process of developing prototype hardware.

## Slide 14: Rover Chassis
No specific requirements around speed or terrain
Simple 4wd frame with motors (~$25)
For prototyping, opt for two wheels plus a caster for easier use
  Tank-style steering does not work well with low powered motors

## Slide 15: Controlling motors
Arduino vs Raspberry Pi vs Beaglebone Black
Decision factors
  Experience with each platform
  Arduino is easy to integrate with motors, connectivity via shields, video (not really)
  Raspberry Pi has large community support, fewer GPIO pins, better multimedia, USB
  Beaglebone Black has more pins for integration, more powerful than Raspberry Pi, smaller community support, USB
  Microcontroller vs Microprocessor
Arduino (~$25), Raspberry Pi (~$40), Beaglebone Black (~$55)

## Slide 16: Providing video
Arduino not a good option
Raspberry Pi has a dedicated camera connection (Camera ~$30)
Beaglebone Black would use a USB webcam

## Slide 17: Android Controller
Handle control input for rover
Display video stream
Connectivity
  WiFi
  Bluetooth

## Slide 18: Let’s Get Started
Assemble chassis and motors
Wire motors to Arduino for testing using a breadboard
Limit the current through the pins
  H-bridge for motor control
  Sparkfun Motor Driver 1A Dual (~$9)

## Slide 19: Arduino UNO

## Slide 20: Programming Arduino
Arduino IDE
Set of C/C++ functions
setup()
loop()

## Slide 21: Programming Arduino
const int STBY = 2;
const int AIN1 = 3;
const int AIN2 = 4;
const int PWMA = 5;
const int BIN1 = 6;
const int BIN2 = 7;
const int PWMB = 9;
const int MOTOR_LEFT = 1;
const int MOTOR_RIGHT = 2;
const int SPEED = 200;
const int fwdPin = 12;
const int backPin = 11;
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 22: Programming Arduino
void setup(){
Serial.begin(9600);
//motor control
pinMode(STBY, OUTPUT);
pinMode(PWMA, OUTPUT);
pinMode(AIN1, OUTPUT);
pinMode(AIN2, OUTPUT);
pinMode(PWMB, OUTPUT);
pinMode(BIN1, OUTPUT);
pinMode(BIN2, OUTPUT);
//button inputs
pinMode(fwdPin, INPUT_PULLUP);
pinMode(backPin, INPUT_PULLUP);
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 23: Programming Arduino
enum DriveState {
forward,
backward,
left,
right,
none
};
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 24: Programming Arduino
void loop(){
DriveState state = getStateFromButtons();
switch(state){
case forward:
goForward(SPEED);
break;
case backward:
goBackward(SPEED);
break;
case left:
turnLeft(SPEED);
break;
case right:
turnRight(SPEED);
break;
default:
stopMotor();
}
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 25: Programming Arduino
DriveState getStateFromButtons(){
int fwd = digitalRead(fwdPin);
int bwd = digitalRead(backPin);
DriveState state = none;
if(fwd == LOW && bwd == LOW){
state = left;
}else if(fwd == LOW){
state = forward;
}else if(bwd == LOW){
state = backward;
}else{
state = none;
}
return state;
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 26: Programming Arduino
void goForward(int speed){
driveMotor(MOTOR_LEFT, speed, 1);
driveMotor(MOTOR_RIGHT, speed, 1);
Serial.println("forward");
}
void goBackward(int speed){
driveMotor(MOTOR_LEFT, speed, 0);
driveMotor(MOTOR_RIGHT, speed, 0);
Serial.println("backward");
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 27: Programming Arduino
void driveMotor(int motor, int speed, int direction){
digitalWrite(STBY, HIGH);
boolean inPin1 = LOW;
boolean inPin2 = HIGH;
if(direction == 1){
inPin1 = HIGH;
inPin2 = LOW;
}
if(motor == MOTOR_LEFT){
digitalWrite(AIN1, inPin1);
digitalWrite(AIN2, inPin2);
analogWrite(PWMA, constrain(speed, 0, 255));
}else if(motor == MOTOR_RIGHT){
digitalWrite(BIN1, inPin1);
digitalWrite(BIN2, inPin2);
analogWrite(PWMB, constrain(speed, 0, 255));
}
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 28: Raspberry Pi

## Slide 29: Raspberry Pi
Raspbian
Python code with GPIO library
Web.py library to provide basic http endpoints
Use 3 pins to signal movement request
  001 – forward
  010 – backward
  011 – left
  100 – right
Additional pin for status

## Slide 30: Programming Raspberry Pi
import RPi.GPIO as GPIO
def init():
GPIO.setmode(GPIO.BCM)
GPIO.setup(18, GPIO.OUT)
GPIO.setup(23, GPIO.OUT)
GPIO.setup(24, GPIO.OUT)
GPIO.setup(25, GPIO.OUT)
GPIO.output(18, True)
def forward():
GPIO.output(23, True)
GPIO.output(24, False)
GPIO.output(25, False)
def backward():
GPIO.output(23, False)
GPIO.output(24, True)
GPIO.output(25, False)
rover.py
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 31: Programming Raspberry Pi
def left():
GPIO.output(23, True)
GPIO.output(24, True)
GPIO.output(25, False)
def right():
GPIO.output(23, False)
GPIO.output(24, False)
GPIO.output(25, True)
def stop():
GPIO.output(23, False)
GPIO.output(24, False)
GPIO.output(25, False)
def cleanup():
GPIO.output(18, False)
GPIO.cleanup()
rover.py
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 32: Programming Raspberry Pi
import atexit, threading, time, web
from rover import *
timer = None
state = 'stop'
urls = (
'/(.*)', 'servicehandler'
)
app = web.application(urls, globals())
def cleanup_rover():
cleanup()
if __name__ == "__main__":
atexit.register(cleanup_rover)
init()
app.run()
rover_service.py
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 33: Programming Raspberry Pi
class servicehandler:
def GET(self, action):
global state
reset_safety()
if not action:
action = 'status'
if action == 'forward':
forward()
state = action
elif action == 'backward':
backward()
state = action
elif action == 'left':
left()
state = action
elif action == 'right':
right()
state = action
elif action == 'stop':
safety_stop()
return state
rover_service.py
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 34: Programming Raspberry Pi
def reset_safety():
global timer
if timer:
timer.cancel()
timer = threading.Timer(5, safety_stop)
timer.start()
def safety_stop():
global state
stop()
state = 'stop'
timer.cancel()
rover_service.py
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 35: Updating Arduino
const int ledPin = 13;
const int pi0 = A0;
const int pi1 = A1;
const int pi2 = A2;
const int pi3 = A3;
//..in setup()..//
pinMode(ledPin, OUTPUT);
//raspberry pi comms
pinMode(pi0, INPUT);
pinMode(pi1, INPUT);
pinMode(pi2, INPUT);
pinMode(pi3, INPUT);
//..in loop ()..//
DriveState state = getStateFromButtons();
if(state == none){
state = getStateFromPi();
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 36: Updating Arduino
DriveState getStateFromPi(){
int p0 = digitalRead(pi0);
int p1 = digitalRead(pi1);
int p2 = digitalRead(pi2);
int p3 = digitalRead(pi3);
if(p3 == HIGH){
digitalWrite(ledPin, HIGH);
if(p0 == HIGH && p1 == LOW && p2 == LOW){
return forward;
}else if(p0 == LOW && p1 == HIGH && p2 == LOW){
return backward;
}else if(p0 == HIGH && p1 == HIGH && p2 == LOW){
return left;
}else if(p0 == LOW && p1 == LOW && p2 == HIGH){
return right;
}else{
return none;
}
}else{
digitalWrite(ledPin, LOW);
}
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 37: Raspberry Pi WiFi
Run as an Access Point to avoid dynamic configuration
DHCP server on board
Static IP address
Issues with drivers and configuration
  Patched version of hostapd with Edimax WiFi dongle
  http://goo.gl/HuamqV

## Slide 38: Raspberry Pi Camera
raspistill and raspivid
mjpg_streamer
  http://goo.gl/52T8nm
mkdir /tmp/stream
raspistill --nopreview -w 640 -h 480 -q 5 -o /tmp/stream/pic.jpg -tl 100 -t 9999999 -th 0:0:0 &
LD_LIBRARY_PATH=/usr/local/lib /usr/local/bin/mjpg_streamer -i "input_file.so -f /tmp/stream -n pic.jpg" -o "output_http.so -w /usr/local/www -p 8081" &

## Slide 39: Android Controller
Basic UI with buttons and webview
Add click handlers for movements
Add way to repeatedly send state

## Slide 40: RoverManager.java
private long lastUpdate;
private String lastCommand;
State currentState = State.Stop;
public enum State {
Forward("forward"),
Backward("backward"),
Left("left"),
Right("right"),
Stop("stop");
private String action;
private State(String action){
this.action = action;
}
public String getAction(){
return action;
}
}
Public State getState(){
return currentState;
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 41: RoverManager.java
public void forward(){
currentState = State.Forward;
}
public void backward(){
currentState = State.Backward;
}
public void left(){
currentState = State.Left;
}
public void right(){
currentState = State.Right;
}
public void stop(){
currentState = State.Stop;
}
private String buildUrl() {
return String.format("http://192.168.3.1:8080/%s", currentState.getAction());
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 42: RoverManager.java
public void sendUpdate(){
//call service on RPi
try {
String command = buildUrl();
long now = System.currentTimeMillis();
if(command != null && (!command.equals(lastCommand) || now - lastUpdate > 4000)){
Log.i(MainActivity.TAG, "Sending update: "+command);
HttpClient httpclient = new DefaultHttpClient();
HttpResponse response = httpclient.execute(new HttpGet(buildUrl()));
StatusLine statusLine = response.getStatusLine();
if (statusLine.getStatusCode() == HttpStatus.SC_OK) {
//..more logic
lastUpdate = System.currentTimeMillis();
lastCommand = command;
} else {
response.getEntity().getContent().close();
}
}
}catch(Exception e){
Log.e(MainActivity.TAG, "exception sending update", e);
}
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 43: MainActivity.java
Handler handler = new Handler();
Runnable updater = new Runnable() {
@Override
public void run() {
AsyncTask updaterTask = new AsyncTask() {
@Override
protected Object doInBackground(Object[] objects) {
roverManager.sendUpdate();
return null;
}
@Override
protected void onPostExecute(Object o) {
super.onPostExecute(o);
if(active) {
handler.postDelayed(updater, 20);
}
}
};
updaterTask.execute();
}
};
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 44: MainActivity.java
@Override
protected void onResume() {
super.onResume();
webView.loadUrl("http://192.168.3.1:8081/stream_simple.html");
active = true;
handler.post(updater);
}
@Override
protected void onPause() {
super.onPause();
active = false;
}
Notes: This meta data tag in AndroidManifest will indicate the version of Play Services that was used in compilation.

## Slide 45: Prototype State and Future
Functions as desired (mostly)
Multi-client access is broken
Power sources are a bit over the top
Chassis maneuverability is disappointing
Consider Beaglebone Black for more processing power and consolidation of components
Polish UI; Add sensor inputs from Android device? (Accel, BT joystick)
On board sensors for autonomous logic. (sonar, light sensor, etc)
Miniaturization with smaller microcontrollers; custom circuit boards.

## Slide 46: Wrap Up
Robotics can be a fun and exciting outlet for trying new ideas.
The same processes and concepts you use for software development really kind of apply to hardware also.
  Break problems into smaller, more manageable tasks
  Define reusable interfaces, decouple functionality, componentize
We worked through a sample prototype with less than a couple hundred dollars in materials.
Whatever your interests, keep your eyes open for opportunities to take advantage of them.
Buy some hardware, hack it together, see what happens.

## Slide 47: Thanks!
Questions?
http://www.arduino.cc
http://www.raspberrypi.org
http://www.beagleboard.org
http://webpy.org
LM2596 Switching Regulator (eBay)
http://www.sparkfun.com
http://www.adafruit.com
Jay Dellinger
google.com/+JayDellinger
@DellingerTech
github.com/jdellinger